## Slide 1
Enhanced QoE Through Personalization
and In-Band Quality Notification
Sergey Gorinsky
IMDEA Networks Institute, Spain
Stellenbosch University, South Africa
7 April 2025
joint work with Leonardo Peroni, Farzad Tashtarian, and Christian Timmerer

## Slide 2
over-the-top (OTT)
streaming providers
Internet
end users
content providers (CPs)
content delivery networks (CDNs)
Internet service providers (ISPs)
2
ingestion
distribution
processing
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
⚠️ The distribution stage must deliver content in real time
Video Streaming Ecosystem
Introduction
iQoE
IQN

## Slide 3
data volume
3
Adaptive Video Streaming by OTT Providers
video segments
(e.g., 4 seconds long)
3
3
3
2
2
2
1
1
1
4
4
4
variable bandwidth
4
3
2
1
4
3
2
1
stall
streaming experience
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
OTT client
end-user device
end user
data center
OTT server
video stream
⚠️ User satisfaction is a key performance objective
Internet
Introduction
iQoE
IQN

## Slide 4
ℹ️ Overall satisfaction with the streaming service as perceived by the user
ℹ️ Measured through subjective assessment
⚠️ Subjective assessments are time-consuming and burdensome
end user
user interface
4
1
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Quality of Experience (QoE)
4
3
2
1
stall
streaming experience
🤔 Can QoE be measured objectively?
Introduction
iQoE
IQN

## Slide 5
5
ℹ️ Multitude of objective IFs
➜ stall duration
➜ image quality
➜ stability of image quality
➜ start-up latency
➜ …
ℹ️ QoE models
➜ defined as functions of IFs
➜ numerous proposals exist
≈
🤔 How are QoE models constructed?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Influence Factors (IFs) and QoE Models
Introduction
iQoE
IQN

## Slide 6
6
score
modeler
score
score
MOSes
experiences
sampler
experiences
experience
…
…
…
MOS
influence factors
…
4
3
2
1
stall
raters
ℹ️ Mean opinion score (MOS) captures the QoE perception by the average rater
QoE model
⚠️ The output is a one-size-fits-all QoE model
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Traditional QoE Modeling
Introduction
iQoE
IQN

## Slide 7
score
modeler
Score
score
MOSes
experiences
sampler
experiences
experience
…
…
…
MOS
influence factors
raters
model
viewer
regular streaming
QoE-based ABR streaming system
viewer
regular streaming
traditional QoE modeling
QoE model
…
7
Usage of the QoE Model by ABR Streaming
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Introduction
iQoE
IQN

## Slide 8
QoE model
all raters
ℹ️ Evaluation on the Waterloo-IV dataset
8
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
⚠️ The one-size-fits-all QoE model is inaccurate of for many users
Diversity of QoE Perception
Introduction
iQoE
IQN

## Slide 9
9
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
© Magritte: This is not an Internet
⚠️ Technical solutions must align with economic realities
Introduction
iQoE
IQN

## Slide 10
$
10
customer
peer
provider
customer
peer
provider
$
$
$
$
$
Thousands of ISPs Organized in Multiple Tiers
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
⚠️ Bilateral ISP agreements hinder offering end-to-end services
Introduction
iQoE
IQN

## Slide 11
no effort, lower QoE
active role
passive role
💡 Providing the user with more opportunities to actively enhance QoE
ℹ️ Who provides these opportunities?
  ➜ OTT providers in individualised QoE (iQoE)
  ➜ ISPs in in-band quality notification (IQN)
⚠️ What are the challenges?
  ➜ Trade-off between user effort and QoE
  ➜ Deployabilty
higher effort, higher QoE
11
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
User Empowerment
Introduction
iQoE
IQN
Notes: Active gives promis of higher QoE
Legacy user

## Slide 12
iQoE: Low-Effort Personalized QoE Modeling
published in ACM CoNEXT 2023 and PACMNET
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN
iQoE
Introduction
12

## Slide 13
Boxplot of 32 HDTV Users of Waterloo-IV dataset
Atypical: 10% furthest from the median QoE perception
⚠️ The inaccuracy is especially high for atypical viewers
atypical raters
(Waterloo-IV dataset)
13
QoE model
all raters
Inaccuracy of a One-Size-Fits-All QoE Model
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Motivation
Design
Subjective Study
Simulations

## Slide 14
🤔 Can the personalization be done with low effort for the viewer?
  💡 Personalization of QoE models
  ❌ Discarded alternatives
    ➜ indirect feedback
    ➜ multiple reference groups
    ➜ tuning of a generic QoE model
  💡 Required feedback
    ➜ explicit input from the viewer
    ➜ must be both expressible and actionable
  💡 The viewer is the sole rater for the personalized model
14
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Our Approach
iQoE
Motivation
Design
Subjective Study
Simulations
Notes: Explain x, inaccurate/not interpretable so we design feebacks, it should came from the same user that consume the content

## Slide 15
viewer
experiences
experience
RIGS sampler
scores
…
score
…
…
…
…
models and scores
influence factors
QoE
model
XSVR modeler
iQoE
experiences
…
💡 Limiting the subjective tests to a small number of experiences
💡 Active learning with new automatic sampler and modeler
  🛠️ Random Improved Greedy Sampling (RIGS)
  🛠️ eXtended Support Vector Regression (XSVR)
15
iQoE (individualised QoE)
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 16
ℹ️ 315 experiences from the Waterloo-IV dataset
ℹ️ Input space: IF values for each experience
ℹ️ Output space: QoE scores assigned to the experiences
better QoE
1-20 (bad) 21-40 (poor) 41-60 (fair) 61-80 (good) 81-100 (excellent)
16
How to Sample the Experience Set Representatively?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 17
⚠️ Quick but with poor coverage of the input space
1-20 (bad) 21-40 (poor) 41-60 (fair) 61-80 (good) 81-100(excellent)
all 315 experiences
50 experiences chosen by RS
17
Random Sampling (RS)
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 18
ℹ️ GS accounts for Euclidean distances in the space of IF values
⚠️ Poor coverage of the output space
50 experiences chosen by RS
50 experiences chosen by GS
1-20 (bad) 21-40 (poor) 41-60 (fair) 61-80 (good) 81-100(excellent)
18
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Greedy Sampling (GS)
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 19
⚠️ Highest complexity with initially small gains
50 experiences chosen by GS
50 experiences chosen by IGS
1-20 (bad) 21-40 (poor) 41-60 (fair) 61-80 (good) 81-100(excellent)
ℹ️ IGS accounts for Euclidean distances in both spaces of IF values and scores
19
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Improved Greedy Sampling (IGS)
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 20
ℹ️ RS for the first h experiences and IGS for experiences h+1 to H
ℹ️ h = 10 and H = 50 experiences empirically
50 experiences chosen by RIGS
1-20 (bad) 21-40 (poor) 41-60 (fair) 61-80 (good) 81-100(excellent)
20
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Our RIGS Sampler
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 21
ℹ️ Support vector regression (SVR)
ℹ️ Set of 10 influence factors as features
  ➜ representation identifier
  ➜ stall duration
  ➜ bitrate
  ➜ chunk size
  ➜ frame width
  ➜ frame height
  ➜ highest bitrate flag
  ➜ peak signal-to-noise ratio (PSNR)
  ➜ structural similarity index measure (SSIM)
  ➜ video multi-method assessment fusion (VMAF)
ℹ️ Waterloo-IV dataset
✅ all are important
according to
permutation
feature importance
21
Our XSVR Modeler
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 22
regular streaming
QoE-based ABR streaming system
regular streaming
QoE models
viewer
experiences
experience
RIGS sampler
scores
…
score
…
…
…
…
models and scores
Influence factors
QoE
model
XSVR modeler
iQoE
experiences
…
22
viewer
viewer
iQoE’s Role in ABR Streaming
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Motivation
Design
Simulations
Subjective Study

## Slide 23
🖥 Browser interface
ℹ️ 120 viewers in total, including 34 direct recruits and the rest from Microworkers
ℹ️ Each viewer rates 120 experiences for training and testing
ℹ️ Each experience consists of four segments
➜ 2-second playback per segment
➜ potential stalls between segments
23
Online Subjective Study with Real Viewers
iQoE
Design
Motivation
Subjective Study
Simulations

## Slide 24
✅ Average MAE decreases at least 42% and 85%
for all raters and atypical raters, respectively
Prominent existing QoE models
Better
24
Accuracy of iQoE vs. Traditional QoE Modeling
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Design
Motivation
Subjective Study
Simulations

## Slide 25
✻ Playback time 7 minutes
✻ Extra time
✻ Expected effort of the viewer 22 minutes
✅ The viewer exerts reasonably low effort
25
Viewer’s Effort
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Design
Motivation
Subjective Study
Simulations

## Slide 26
8 QoE models scores of 32 real raters 256 synthetic raters
ℹ️ Extending real-world experiments to systematically evaluate:
  ➜ design choices
  ➜ parameter sensitivity
  ➜ overhead
ℹ️ Introducing a novel synthetic profiling technique:
  ➜ 256 synthetic raters, each assessing 1,000 experiences
26
Simulations
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Design
Subjective Study
Motivation
Simulations

## Slide 27
✅ iQoE consistently outperforms design alternatives
iQoE RIGS + Extreme Gradient Boosting
RIGS + Random Forest RIGS + Gaussian Process
Better
27
Sensitivity to the Modeler Choice
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Design
Subjective Study
Motivation
Simulations

## Slide 28
✅ Processing and memory overhead of iQoE is negligible
Average Standard deviation
Switch from RS to IGS
28
iQoE Per-Iteration Time
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
iQoE
Design
Subjective Study
Motivation
Simulations

## Slide 29
29
SocialProbing (TED2021-131264B-I00)
funded by
GreenEdge (PID2021-128223OA-I00)
funded by
Christian Doppler Laboratory ATHENA
funded by
Acknowledgments
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN
iQoE
Introduction

## Slide 30
✻ iQoE: A new method for personalizing QoE models
💡Active learning, RIGS sampler, XSVR modeler
✻ Evaluation
🛠️ Online subjective study with 120 real viewers
🛠️ Simulations
✻ Results
  ✅ Accuracy improvement: 85% (42%) on average for atypical (all) viewers
  ✅ Viewer effort: 50 assessments, total training time: 22 minutes
30
Dataset and code available at: https://github.com/Leo-rojo/iQoE_Dataset_and_Code
ACM badges, among three papers selected for the Artifacts Session, CoNEXT 2023
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Conclusions
IQN
iQoE
Introduction
Notes: Mention code

## Slide 31
IQN: In-Band Quality Notification from Users to ISPs
published in IEEE CloudNet 2024
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
31
Introduction
iQoE
IQN

## Slide 32
Why do Internet service providers (ISPs) struggle
with quality of experience (QoE) management?
32
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Motivation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 33
33
ISPs Have the Means and Incentives to Improve QoE
3
2
stall
ISP
insufficient bandwidth
end-user device
end user
⚠️ But first, ISPs must detect QoE impairment
impaired QoE
🛠️ Means
➜ traffic prioritization
➜ rerouting
💰 Incentives
➜ connectivity market competitiveness
➜ customer attraction and retention
video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 34
34
Independent ISP-Side QoE Inference Is Challenging
ISP
🤔 Who might assist ISPs in QoE inference?
OTT client
end-user device
end user
ℹ️ OTT providers encrypt traffic end-to-end, e.g., with QUIC
❌ Encryption renders deep packet inspection (DPI) ineffective
❌ Independent learning-based QoE inference struggles with accuracy
QoE?
data center
OTT server
encrypted video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 35
35
Potential Assistants in ISP-Side QoE Inference
⚠️ End users require a mechanism for notifying ISPs of QoE
❌ OTT providers
➜ control QoE on their own and have little incentive to share insights with ISPs
✅ End users
➜ directly benefit from QoE improvement and have access to QoE information
ISP
end-user device
end user
QoE?
encrypted video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
data center
OTT client
OTT server
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 36
36
access ISP
ℹ️ Internet operates through bilateral agreements
➜ e.g., between an end user and access ISP
⚠️ The bandwidth bottleneck might be in other ISPs
The End User Is Aware of the Access ISP Only
⚠️ Need to notify ISPs beyond the access provider
bottleneck ISP
OTT client
end-user device
end user
encrypted video stream
insufficient bandwidth
bilateral relationship
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 37
⚠️ Notifications must reach ISPs along the server-to-client path
37
Asymmetric Routing Complicates Notifications
access ISP
bottleneck ISP
end-user device
end user
encrypted video stream
insufficient bandwidth
ℹ️ The bottleneck ISP might be off the client-to-server path
data center
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
OTT client
OTT server
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 38
38
Network Address Translation (NAT) Alters Flows
⚠️ The notification mechanism must function despite NAT
access ISP
bottleneck ISP
OTT client
end-user device
end user
encrypted video stream
insufficient bandwidth
NAT
ℹ️ NAT modifies the identifiers of network flows
ℹ️ The same video stream has different flow identifiers
➜ flow X in the bottleneck ISP
➜ flow Y in the end-user device
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 39
39
✻ Design a mechanism that:
➜ enables the end user of the OTT streaming service to signal QoE
➜ notifies ISPs beyond the access provider along the server-to-client path
✻ With no support from the OTT provider
✻ Despite end-to-end traffic encryption, asymmetric routing, and NAT
Problem Statement
QoE
ISP
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
OTT server
OTT client
❌
❌
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 40
40
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Related Work
How do end users and remote ISPs communicate today?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 41
41
Application-Layer Traffic Optimization (ALTO)
ISP
❌ ALTO does not provide application information to ISPs
ALTO client
end-user device
ℹ️ IETF RFC 7285
ℹ️ Exposes network topologies, routing preferences, and cost maps to applications
ℹ️ Enables the client in its selection of another endpoint, e.g., a server or a peer
ALTO server
queries
network information
ALTO protocol
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 42
42
CAMARA Quality on Demand (QoD)
❌ CAMARA QoD struggles to identify remote ISPs and right flows
ℹ️ Application programming interface (API) of Linux Foundation’s CAMARA project
ℹ️ Out-of-band signaling from applications to ISPs, mostly mobile providers
ℹ️ Enables applications to request network quality upgrades
bottleneck ISP
OTT client
end-user device
data center
OTT server
request
QoD API
QoD API
upgrade
access ISP
NAT
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 43
43
Network Cookies
❌ Network cookies require OTT support to reach server-to-client ISPs
access ISP
bottleneck ISP
end-user device
encrypted video stream
insufficient bandwidth
OTT server
ℹ️ Stanford, ACM SIGCOMM 2016
ℹ️ User-inserted metadata in packets
ℹ️ Enable users to signal preferences
➜ to ISPs and OTT providers
data center
NAT
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
end user
OTT client
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 44
44
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Solution
How do we advance the state of the art?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 45
45
IQN (In-band Quality Notification)
ℹ️ New general mechanism for QoE signaling from end users to ISPs
➜ adaptable to different OTT services and QoE signals
➜ building block for QoE management protocols
ℹ️ Two core (automated) components:
➜ user agent (sender)
➜ ISP agent (receiver)
ISP agent
OTT client
user agent
end-user device
ISP
QoE
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 46
46
Key Insights
💡To engage with the user, the OTT client exposes interactive features:
OTT client
user agent
OTT client
OTT server
QoE
ISP agent
💡 Which the user agent leverages to induce:
➜ a distinctive packet pattern in client-to-server traffic
ℹ️ The OTT server reacts by generating:
➜ a distinctive packet pattern in server-to-client traffic
💡 This enables the ISP agent to infer QoE:
➜ from the observed server-to-client packet pattern
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 47
47
Putting It All Together
✅ IQN successfully notifies server-to-client ISPs of QoE
access ISP
bottleneck ISP
end user
OTT server
end-user device
data center
NAT
ISP agent
QoE
OTT client
user agent
✅ compatible with NAT
✅ requires no support from the OTT provider
✅ works despite encryption, asymmetric routing
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 48
48
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Implementation
Is IQN feasible?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 49
ℹ️ OTT service: YouTube
ℹ️ QoE signal: video stall
ℹ️ OTT client’s interactive feature: autoplay switch
ℹ️ Inducing a distinctive packet pattern:
➜ toggle autoplay even times (4 toggles) with short intervals (5 ms)
➜ periodically repeat while a stall persists
ℹ️ Inferring QoE from server-to-client packet timing: ● ● ● ● ● ● ● ● ● ● ● ● ● ● ●
➜ identify candidate packets (size: 1,180 – 1,288 bytes)
➜ apply two sliding windows over packet arrivals to detect stall start and end
IQN Instantiation in YouStall
49
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 50
ℹ️ Recognition of YouTube’s spinning icon in periodic screenshots
Stall Detection by YouStall’s User Agent
50
stall
stall
stall
time
🔄 Alternative: YouTube’s Stats for Nerds
YouStall code available at https://github.com/Leo-rojo/IQN_YouStall_Code_CloudNet_2024
no stall
no stall
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 51
51
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Evaluation
Is IQN effective in our prototype?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 52
Experimental Topology
ℹ️ End-user device
➜ runs YouStall’s user agent
ℹ️ Amazon Elastic Compute Cloud (EC2) instance
➜ emulates an ISP and hosts YouStall’s ISP agent
➜ tunnels user traffic over OpenVPN before sending it over the public Internet
EC2, Frankfurt
OpenVPN
52
end-user device, Madrid
user agent
YouTube server
data center
YouTube client
ISP agent
Internet
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 53
Experimental Settings
ℹ️ YouTube Live videos
➜ three genres: news, music, and sports
➜ played automatically in Google Chrome
ℹ️ Stalls
➜ 100 per genre
➜ traffic limited to 1 Mbps using tcconfig
➜ resolution fixed at 720p
➜ ground truth: tracking via the ytp-spinner tag in Selenium
➜ timelines synchronized with screenshot timelines
ℹ️ Memory and processing overhead
➜ measured using psutil
53
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 54
✅ IQN enables YouStall to accurately detect actual stalls at the ISP
Operational Example
on the end-user device
at the ISP
54
candidate packet number
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 55
✅ YouStall accurately infers stall-duration distributions
Duration of Inferred vs. Actual Stalls
55
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 56
✅ YouStall estimates the duration of significant stalls with low error
Duration Error for Significant Stalls
✻ Stall duration
➜ average
● 1.4 s
➜ significant
● at least 400 ms
✻ Average error
➜ 200-300 ms
56
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 57
57
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Discussion
What are open questions and challenges?
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 58
Integrating IQN into QoE Management Protocols
✻ Coordination between multiple server-to-client ISPs
❌ requires an additional explicit mechanism
✅ each ISP acts independently
✻ ISP action while receiving IQN signals
❌ enforces absolute per-domain performance levels (like CAMARA QoD)
✅ grants relatively higher priority to the video flow on each traversed link
58
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
OTT client
OTT server
IQN
IQN
IQN
IQN
QoE
⏫
ISPs
⏫
⏫
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 59
Additional Considerations
✻ Deployment
✅ by an ISP, an ISP consortium, or a third party
✻ Dynamic maintenance
🔄 standard practice in modern software
✻ Deliberate disruption of IQN signaling by OTT providers
⚠️ may trigger neutrality regulations for OTT providers
✻ Scalability of OTT-specific IQN instantiation
✅ feasible due to the relatively small number of OTT hypergiants
✻ Privacy
🔒 IQN shares only QoE information, not video content
59
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 60
IQN Relevance to ISPs
✻ Establishing a direct relationship with end users
✅ particularly beneficial for remote ISPs
✻ Enhancing QoE at a network-layer timescale
✅ reacts within hundreds of milliseconds
✅ faster than OTT providers' application-layer adjustments (seconds)
✻ Monetization opportunities
💰 subscription-based services
💰 advertisements in IQN’s user agents on end-user devices
60
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 61
Future Work
📊 Further research on IQN
➜ stalls vs. other QoE metrics
➜ binary impairment signaling vs. QoE value encoding
🛠️ IQN integration into QoE management
➜ developing new mechanisms for QoE detection by user agents
➜ exploring techniques for QoE improvement by ISPs
➜ studying fairness considerations
🔗 Extending IQN to additional OTT services
🤝 Collaborating with ISPs for real-world IQN experimentation
📜 Advancing IQN standardization efforts
61
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
IQN

## Slide 62
62
DRONAC (PID2022-140560OB-I00)
funded by
MICIU/AEI/10.13039/501100011033 and ERDF, EU
Christian Doppler Laboratory ATHENA
funded by
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Acknowledgments
Introduction
iQoE
IQN

## Slide 63
✻ Problem
❌ ISPs struggle to infer QoE, limiting their ability to improve it
❌ existing solutions (e.g., ALTO and CAMARA QoD) do not fully bridge the gap
✻ In-band Quality Notification (IQN): a new mechanism
✅ enables end users to notify ISPs of QoE
✅ works despite encryption, asymmetric routing, and NAT
✅ requires no OTT support
✻ Next steps
🛠️ IQN integration into QoE management
🛠️ real-world testing
🛠️ standardization
63
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Conclusions
Introduction
iQoE
IQN

## Slide 64
✻ Video streaming: a diverse and evolving ecosystem
➜ involves multiple diverse stakeholders: ISPs, OTT providers, end users
➜ shaped by new technical mechanisms and business models
✻ iQoE: Low-effort personalization of QoE model
✅ builds an accurate QoE model for individual users
✅ uses active learning to efficiently adapt to user preferences
✻ IQN: In-band QoE signaling
✅ enables QoE signaling from end users to ISPs
✅ leverages the OTT client’s interface
✅ requires no support from OTT providers
64
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University
Overall Summary
Introduction
iQoE
IQN

## Slide 65
Backup Slides
Sergey Gorinsky, “Enhanced QoE Through Personalization and In-Band Quality Notification”, Stellenbosch University

## Slide 66
Inaccuracy of Traditional QoE Modeling
Waterloo-IV dataset
66

## Slide 67
Results of the Subjective Studies
67

## Slide 68
iQoE Dataset
68

## Slide 69
iQoE vs. Traditional QoE Modeling
69

## Slide 70
70
iQoE vs. Traditional QoE Modeling

## Slide 71
iQoE vs. Personalized QoE Modeling
71

## Slide 72
Sensitivity to the Modeler and Sampler Choices
72

## Slide 73
Sensitivity to Parameter h and Training-Set Share
73

## Slide 74
iQoE Processing and Memory Overhead
74