## Slide 1
Sergey Gorinsky
IMDEA Networks Institute, Spain
Amazon Web Services, online presentation
12 June 2025
joint work with Leonardo Peroni and Farzad Tashtarian
IQN: In-Band Quality Notification

## Slide 2
Why do Internet service providers (ISPs) struggle
with quality of experience (QoE) management?
2
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Motivation

## Slide 3
data volume
3
Motivation
Related Work
Solution
Implementation
Evaluation
Over-The-Top (OTT) Adaptive Video Streaming
video segments
(e.g., 4 seconds long)
3
3
3
2
2
2
1
1
1
4
4
4
variable bandwidth
4
3
2
1
4
3
2
1
stall
QoE
ISP
OTT client
end-user device
end user
data center
OTT server
video stream
⚠️ QoE improvement is a key objective
Discussion
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 4
4
ISPs Have the Means and Incentives to Improve QoE
3
2
stall
ISP
insufficient bandwidth
end-user device
end user
⚠️ But first, ISPs must detect QoE impairment
impaired QoE
🛠️ Means
➜ traffic prioritization
➜ rerouting
💰 Incentives
➜ connectivity market competitiveness
➜ customer attraction and retention
video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 5
5
Independent ISP-Side QoE Inference Is Challenging
ISP
🤔 Who might assist ISPs in QoE inference?
OTT client
end-user device
end user
ℹ️ OTT providers encrypt traffic end-to-end, e.g., with QUIC
❌ Encryption renders deep packet inspection (DPI) ineffective
❌ Independent learning-based QoE inference struggles with accuracy
QoE?
data center
OTT server
encrypted video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 6
6
Potential Assistants in ISP-Side QoE Inference
⚠️ End users require a mechanism for notifying ISPs of QoE
❌ OTT providers
➜ control QoE on their own and have little incentive to share insights with ISPs
✅ End users
➜ directly benefit from QoE improvement and have access to QoE information
ISP
end-user device
end user
QoE?
encrypted video stream
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
data center
OTT client
OTT server
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 7
7
access ISP
ℹ️ Internet operates through bilateral agreements
➜ e.g., between an end user and access ISP
⚠️ The bandwidth bottleneck might be in other ISPs
The End User Is Aware of the Access ISP Only
⚠️ Need to notify ISPs beyond the access provider
bottleneck ISP
OTT client
end-user device
end user
encrypted video stream
insufficient bandwidth
bilateral relationship
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 8
8
Network Address Translation (NAT) Alters Flows
⚠️ The notification mechanism must function despite NAT
access ISP
bottleneck ISP
OTT client
end-user device
end user
encrypted video stream
insufficient bandwidth
NAT
ℹ️ NAT modifies the identifiers of network flows
ℹ️ The same video stream has different flow identifiers
➜ flow X in the bottleneck ISP
➜ flow Y in the end-user device
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 9
⚠️ Notifications must reach ISPs along the server-to-client path
9
Asymmetric Routing Complicates Notifications
access ISP
bottleneck ISP
end-user device
end user
encrypted video stream
insufficient bandwidth
ℹ️ The bottleneck ISP might be off the client-to-server path
data center
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
OTT client
OTT server
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 10
10
✻ Design a mechanism that:
➜ enables the end user of the OTT streaming service to signal QoE
➜ notifies ISPs beyond the access provider along the server-to-client path
✻ With no support from the OTT provider
✻ Despite end-to-end traffic encryption, NAT, and asymmetric routing
Problem Statement
QoE
ISP
Motivation
Related Work
Solution
Implementation
Evaluation
Discussion
OTT server
OTT client
❌
❌
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 11
11
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Related Work
How do end users and remote ISPs communicate today?
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 12
12
Application-Layer Traffic Optimization (ALTO)
ISP
❌ ALTO does not provide application information to ISPs
ALTO client
end-user device
ℹ️ IETF RFC 7285
ℹ️ Exposes network topologies, routing preferences, and cost maps to applications
ℹ️ Enables the client in its selection of another endpoint, e.g., a server or a peer
ALTO server
queries
network information
ALTO protocol
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 13
13
CAMARA Quality on Demand (QoD)
❌ CAMARA QoD struggles to identify remote ISPs and right flows
ℹ️ Application programming interface (API) of Linux Foundation’s CAMARA project
ℹ️ Out-of-band signaling from applications to ISPs, mostly mobile providers
ℹ️ Enables applications to request network quality upgrades
bottleneck ISP
OTT client
end-user device
data center
OTT server
request
QoD API
QoD API
upgrade
access ISP
NAT
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 14
14
Network Cookies
❌ Network cookies require OTT support to reach server-to-client ISPs
access ISP
bottleneck ISP
end-user device
encrypted video stream
insufficient bandwidth
OTT server
ℹ️ Stanford, ACM SIGCOMM 2016
ℹ️ User-inserted metadata in packets
ℹ️ Enable users to signal preferences
➜ to ISPs and OTT providers
data center
NAT
Solution
Implementation
Evaluation
Discussion
Motivation
Related Work
end user
OTT client
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 15
15
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Solution
How do we advance the state of the art?
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 16
16
In-Band Quality Notification (IQN)
ℹ️ New general mechanism for QoE signaling from end users to ISPs
➜ adaptable to different OTT services and QoE signals
➜ building block for QoE management protocols
ℹ️ Two core (automated) components:
➜ user agent (sender)
➜ ISP agent (receiver)
ISP agent
OTT client
user agent
end-user device
ISP
QoE
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 17
17
IQN Key Insights
💡To engage with the user, the OTT client exposes interactive features:
OTT client
user agent
OTT client
OTT server
QoE
ISP agent
💡 Which the user agent leverages to induce:
➜ a distinctive packet pattern in client-to-server traffic
ℹ️ The OTT server reacts by generating:
➜ a distinctive packet pattern in server-to-client traffic
💡 This enables the ISP agent to infer QoE:
➜ from the observed server-to-client packet pattern
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 18
18
IQN: Putting It All Together
✅ IQN successfully notifies server-to-client ISPs of QoE
access ISP
bottleneck ISP
end user
OTT server
end-user device
data center
NAT
ISP agent
QoE
OTT client
user agent
✅ compatible with NAT
✅ works despite encryption, asymmetric routing
✅ requires no support from the OTT provider
Implementation
Evaluation
Discussion
Motivation
Solution
Related Work
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 19
19
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Implementation
Is IQN feasible?
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 20
ℹ️ OTT service: YouTube
ℹ️ QoE signal: video stall
ℹ️ OTT client’s interactive feature: autoplay switch
ℹ️ Inducing a distinctive packet pattern:
➜ toggle autoplay even times (4 toggles) with short intervals (5 ms)
➜ periodically repeat while a stall persists
ℹ️ Inferring QoE from server-to-client packet timing: ● ● ● ● ● ● ● ● ● ● ● ● ● ● ●
➜ identify candidate packets (size: 1,180 – 1,288 bytes)
➜ apply two sliding windows over packet arrivals to detect stall start and end
IQN Instantiation in YouStall
20
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 21
ℹ️ Recognition of YouTube’s spinning icon in periodic screenshots
Stall Detection by YouStall’s User Agent
21
stall
stall
stall
time
🔄 Alternative: YouTube’s Stats for Nerds
YouStall code available at https://github.com/Leo-rojo/IQN_YouStall_Code_CloudNet_2024
no stall
no stall
Evaluation
Discussion
Motivation
Implementation
Related Work
Solution
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 22
22
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Evaluation
Is IQN effective in our prototype?
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 23
Experimental Topology
ℹ️ End-user device
➜ runs YouStall’s user agent
ℹ️ Amazon Elastic Compute Cloud (EC2) instance
➜ emulates an ISP and hosts YouStall’s ISP agent
➜ tunnels user traffic over OpenVPN before sending it over the public Internet
EC2, Frankfurt
OpenVPN
23
end-user device, Madrid
user agent
YouTube server
data center
YouTube client
ISP agent
Internet
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 24
Experimental Settings
ℹ️ YouTube Live videos
➜ three genres: news, music, and sports
➜ played automatically in Google Chrome
ℹ️ Stalls
➜ 100 per genre
➜ traffic limited to 1 Mbps using tcconfig
➜ resolution fixed at 720p
➜ ground truth: tracking via the ytp-spinner tag in Selenium
➜ timelines synchronized with screenshot timelines
ℹ️ Memory and processing overhead
➜ measured using psutil
24
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 25
✅ IQN enables YouStall to accurately detect actual stalls at the ISP
Operational Example
on the end-user device
at the ISP
25
candidate packet number
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 26
✅ YouStall accurately infers stall-duration distributions
Duration of Inferred vs. Actual Stalls
26
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 27
✅ YouStall estimates the duration of significant stalls with low error
Duration Error for Significant Stalls
✻ stall duration
➜ average
● 1.4 s
➜ significant
● at least 400 ms
✻ average error
➜ 200-300 ms
27
Discussion
Motivation
Evaluation
Related Work
Solution
Implementation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 28
28
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Discussion
What are open questions and challenges?
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 29
Integrating IQN into QoE Management Protocols
✻ Coordination between multiple server-to-client ISPs
❌ requires an additional explicit mechanism
✅ each ISP acts independently
✻ ISP action while receiving IQN signals
❌ enforces absolute per-domain performance levels (like CAMARA QoD)
✅ grants relatively higher priority to the video flow on each traversed link
29
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
OTT client
OTT server
IQN
IQN
IQN
IQN
QoE
⏫
ISPs
⏫
⏫
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 30
Additional Considerations
✻ Deployment
✅ by an ISP, an ISP consortium, or a third party
✻ Dynamic maintenance
🔄 standard practice in modern software
✻ Deliberate disruption of IQN signaling by OTT providers
⚠️ may trigger neutrality regulations for OTT providers
✻ Scalability of OTT-specific IQN instantiation
✅ feasible due to the relatively small number of OTT hypergiants
✻ Privacy
🔒 IQN shares only QoE information, not video content
30
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 31
IQN Relevance to ISPs
✻ Establishing a direct relationship with end users
✅ particularly beneficial for remote ISPs
✻ Enhancing QoE at a network-layer timescale
✅ reacts within hundreds of milliseconds
✅ faster than OTT providers' application-layer adjustments (seconds)
✻ Monetization opportunities
💰 subscription-based services
💰 advertisements in IQN’s user agents on end-user devices
31
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 32
Future Work
📊 Further research on IQN
➜ stalls vs. other QoE metrics
➜ binary impairment signaling vs. QoE value encoding
🛠️ IQN integration into QoE management
➜ developing new mechanisms for QoE detection by user agents
➜ exploring techniques for QoE improvement by ISPs
➜ studying fairness considerations
🔗 Extending IQN to additional OTT services
🤝 Collaborating with ISPs for real-world IQN experimentation
32
Motivation
Discussion
Related Work
Solution
Implementation
Evaluation
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 33
33
DRONAC (PID2022-140560OB-I00)
funded by
MICIU/AEI/10.13039/501100011033 and ERDF, EU
Christian Doppler Laboratory ATHENA
funded by
Acknowledgments
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12

## Slide 34
✻ Problem
❌ ISPs struggle to infer QoE, limiting their ability to improve it
❌ existing solutions (e.g., ALTO and CAMARA QoD) do not fully bridge the gap
✻ In-band Quality Notification (IQN): a new mechanism
✅ enables end users to notify ISPs of QoE
✅ works despite encryption, asymmetric routing, and NAT
✅ requires no OTT support
✻ Next steps
🛠️ IQN integration into QoE management and real-world testing
🙌 Let us explore the possibilities together!
34
Conclusions
Sergey Gorinsky, “In-Band Quality Notification from Users to ISPs”, AWS online, 2025/6/12